COMS Sea Surface Temperature Algorithm

Kyung-Ae Park1,2

1RIO / Dep. of Earth Science Education, Seoul National University, Seoul, Korea

2Department of Earth Science Education, Seoul National University, Seoul, Korea

Sea surface temperature is one of the most important atmospheric and oceanic parameters. Need for the accurate assessment of SST has been increased for understanding diverse oceanic phenomena and air-sea interactions. The first Korean meteorological-oceanic geostationary satellite COMS has a MI (Meteorological Imager) sensor for sea surface temperature retrieval. COMS SST algorithms were developed by using the Japanese geostationary satellite MTSAT-1R data and also developed by theoretical approach based on RTM (Radiative Transfer Model). MTSAT-1R had been well operated for several years and produced high quality of visible images and sea surface temperature (SST) images. Using MTSAT-1R data, we derived MTSAT-1R SST coefficients and used to develop a real-time SST retrieval software for COMS satellite by considering COMS response functions of each channel. Match-up database between satellite-tracked drifters and MTSAT-1R data were produced and used for the retrieval procedure of SST coefficients. Newly-derived MCSST equations showed an RMS errors of less than 0.84~0.89oC. We introduced real-time operational process and post-process for COMS SST and also discussed the error characteristics of the MTSAT-1R SST equations by examining their spatial and temporal variations and relation to atmospheric and oceanic environment.